## Slide 1
Generator Energy Storage Integrated System (GENESIS)
Electrical Accumulator Unit (EAU)
Preliminary Design Review
(PDR)
January 14, 2020
WARNING - This document contains technical data whose export is restricted by the Arms Export Control Act (Title 22, U.S. C., Sec 2751, et seq.) International Traffic in Arms Regulations (ITAR). Disclosure to foreign persons without prior U.S. Government approval is prohibited. Violations of these export laws/regulations are subject to severe criminal penalties.

## Slide 2: Introductions/Agenda (Times are EST)

## Slide 3: PDR Objectives
Review progress made since SRR.
Present data/methods being implemented to arrive at the final design including:
  DC/DC Converter trade-offs
  Capacitor trade-offs
  Capacitor Management System trade-offs
  FP note: System Mass & size estimates
  ICD
  GUI
  Machine states
  Simulation models (Output response & RB Note: Executable System Driver?)
Review requirements metrics; compliance and verification.
Identify program risk and opportunities.
Program management including schedule, staffing, deliverables and action items.

## Slide 4: Program Overview

## Slide 5: FP note: Summary of Requirements - 1
Frank P add content
RB note: I placed “Summary of Requirements – 1” as title, I believe that was FP’s intent

## Slide 6: Summary of Requirements - 2
Frank P to add content
RB note: I placed “Summary of Requirements – 2” as title, I believe that was FP’s intent

## Slide 7: Results Of Trade Studies

## Slide 8: DC-DC Converter (MarcoA to add content)
FP note: – Why this type of DC-DC versus another

## Slide 9: System Performance
Take-aways from HESM trade-study results:
  For high-pulse power applications with short time-duration such as GENESIS EAU and HESM, actual amount of energy storage (capacitance) is unimportant. Only low ESR matters to maximize terminal voltage during high power load transients
  In such applications, ultracapacitors with lowest Mass and ESR product win (smallest size, lowest loss, smallest converter)
  Adding capacitors is significantly cheaper/smaller than adding converter phase legs (i.e., higher ESD voltage vs. additional converter current capability)
System Power Loss vs. Weight
1s Peak RMS Current vs. Weight

## Slide 10: DC-DC Converter, Topology
EAU Converter Topology
  PCKA’s EAU hardware has traditionally utilized a boost converter as it provides best utilization of ultracapacitor energy storage. However, in previous applications the short-circuit behavior of the converter was determined to be acceptable or, in some cases, desirable, with short-circuit considerations handled at a system level.
  EAU converter will be a 4-switch bi-directional buck-boost converter, which allows same advantages as boost converter but addresses short-circuit current feeding requirements (full control of current into short through buck-portion of converter)
  EAU converter will operate in boost-mode under normal operation and in buck-mode when bus voltage is lower than ESD voltage
  Topology doubles number of device phase-legs, but only marginally increases loss as only one phase-leg is actively switching. Size/weight is also only affected marginally as EMI-filter remains the same
Property | Buck Converter | Boost Converter | Boost-Buck Converter (Traditional) | Isolated Converter | 4-Switch Bi-Directional Buck-Boost Converter
Bi-Directionality | Yes | Yes | Yes | Yes | Yes
ESD Voltage Range | Vdc up to device limits. Can yield undesirably high dc voltages at high altitudes | Ideally 0 to Vdc Realistic about 1:3 boost ratio | Ideally 0 to device limits Switches see Vdc + VESD Results in high voltages at high altitude | Up to device limits, no restrictions | Same as boost converter
Size / Mass | Small (single phase-leg, inductor) | Small (single phase-leg, inductor) | Small (single phase leg, inductor) | Big (four phase-legs plus HF transformer) | Medium (requires additional phase leg)
Converter Loss | Low | Low | High (high switching loss as devices see Vdc + VESD) | Low to medium, depending on control implementation | Low (additional phase leg is conduction loss only)
Simplicity (Control, Impl.) | Simple, but may require ESD precharge | Simple | Simple | Complex | Simple
Short-Circuit, Bus | Full control of current | Diode path, no control | Full control of current | Full control of current | Full control of current
Short-Circuit, ESD | Diode path, no control | Full control of current | Full control of current | Full control of current | Full control of current

## Slide 11: DC-DC Converter, Sizing
Trade-off between dc-dc converter and ESD size
  Each dc-dc converter GaN phase leg can approximately handle 150 A peak current for 50 – 100 ms
  Each phase-leg adds about 1.5 kg of weight to the converter (incl. inductor, heatsink, housing increase)
  Ultracapacitor cells are assumed to be operated at 2.55 Vdc (2.7 Vdc max)
  Yunasko 1200 F ultracapacitor cell has 0.3 kg weight, 0.3 mΩ ESR (includes connection resistance)
Constraints:
  At this time, cannot have more than 8 phase-legs per converter power stage module without additional size/weight penalty
  Limit max. ultracapacitor bank voltage to 250 Vdc to allow control headroom into 270 Vdc bus
Trade-Off Converter vs. Ultracapacitor Size
UC Terminal Voltage and Current vs. Size
Note:
Mass number is combined phase-legs and ultracapacitors, but represents only active portion and does not include housing and auxiliary components (fixed mass).

## Slide 12: Energy Storage Device (ESD) (FrankP to add content)
FP note: – Comparison of capacitor types

## Slide 13: Energy Storage Device (ESD) Capacitor Trade-Offs and Selection

## Slide 14
The total power requirements are thus the startup and turn off the DEW and the DEW and the noise suppression requirements
  For the 36kW noise requirement, we assume a 41kW total pull from the ESD (+14%) from the EAU
  For the 150kW DEW, we assume 180kW from the EAU
We also note that the noise suppression during the DEW pulse is reduced.

## Slide 15: Noise Current (at 41kW)
24in wide

## Slide 16
50mV delta at start of discharge but 150mV OCV delta

## Slide 17: Intercells
The Skeleton Caps require an intercell connector. The Yunasko’s do not

## Slide 18: Vacuum

## Slide 19: From
From this initial chart we were able to downselect to the Skeleton and Yunasko Capacitors
The customer indicated that cooling the capacitor bank was not desired.
Because we had the ESR, and a duty cycle, and a mass and a heat capacity we were able to calculate the adiabatic temperature rise rate

## Slide 20: Average Current
From this initial chart we were able to downselect to the Skeleton and Yunasko Capacitors
The customer indicated that cooling the capacitor bank was not desired.
Because we had the ESR, and a duty cycle, and a mass and a heat capacity we were able to calculate the adiabatic temperature rise rate

## Slide 22: Adiabatic Run time
Longer runtimes are likely to deviate from adiabatic more.
37 min
19 min

## Slide 23: Review Of Preliminary Design

## Slide 24: DC-DC Converter (MarcoA to add content)

## Slide 25: EAU Concept Diagram

## Slide 26: DC-DC Converter Module Diagram

## Slide 27: DC-DC Converter, Components
Component | Description | Part Number / Series | Supplier
Power Stage Module (PSM) | GaN-based, 8 phase-leg, including measurements | PCA_PCKA_146C | PCKA
Primary Filter Inductors | Nanocrystalline inductors, custom | TBD | MK Magnetics
EMI-Filter, ESD | ESD-side DM and CM EMI-Filter, PCB based | TBD | PCKA
EMI-Filter, 270 V Bus | Bus-side DM and CM EMI-Filter, PCB based | TBD | PCKA
Main Control Module (MCM) | DSP control PCB, based on TI TMS320F28377D | PCA_PCKA_138A | PCKA
Peripheral Expansion Module (PEM) | PCB between MCM and peripheral equipment. Controls contactors, isolates digital I/O lines, analog measurements, and communication | TBD | PCKA
Control Power Module (CPM) | Isolated 24 Vdc for EAU internal, derived from 28 V, 270 V, and/or ESD voltage | TBD | PCKA
MLC | Main-line contactor | KHR503 | TE Connectivity
Current sensor (int. & ext.) | Current sensor, closed-loop hall effect, +/- 1000 A | LF 1010-S | LEM
Heatsink | Micro-channel coldplate, custom aluminum, interfacing with PSM, primary inductors | TBD | Wieland Microcool
Power Connectors | Single-pole. 500 A power connectors with straight exit option | HBB Series | Smiths Interconnect
Signal Connectors | Circular connectors, D38999 Series III, M-Series (EN-plated composite) | D38999/XXM | Wesco Aircraft
Indicators | LED, 8mm, panel mount, IP67 | Q8 Series | APEM / PEI Genesis
Housing | Aluminum, black anodized MIL-A-8625, Type 2, Class 2 | TBD | TBD
Sealing | O-ring, Fluorosilicone (-62 to 205ºC) | TBD | McMaster
Pressure Equalizer | Gore PolyVent stainless steel (-40 to 125ºC) | PMF200444 | Sealing Devices

## Slide 28: DC-DC Converter, CAD Model
Converter box, with and without lid
Mass
Front Panel layout (connectors, cooling)
How do we survive environment (conformal coating, sealing, venting)
How are performance requirements addressed (underlying design assumption, corner operating points)?

## Slide 29: Capacitor Bank (FrankP to add content)

## Slide 30: Capacitor Bank (FrankP to add content)

## Slide 31: Capacitor Management System (CMS) (RayS to add content)
Architecture

## Slide 32: State Diagram & Software Requirements

## Slide 33: DC-DC Converter (MarcoA to provide Content)
MA Email Text from 20191231
“Slide 19: Software Requirements? I think software requirements refers to the simulation models, not the controls of the EAU (there is no software per se, it’s code implemented on a DSP)”

## Slide 34: DC-DC Converter Control
Control state diagrams including
  Startup
  BIT, PBIT
  Normal operation
  Fault

## Slide 35: Capacitor Management System (CMS) (RayS to provide content)

## Slide 36: Simulation Models

## Slide 37: DC-DC Converter (MarcoA to provide content)
Output response

## Slide 38: EAU Simulation Model
Simulation results for expected load profiles
  Electrical, Thermal
Software user manual

## Slide 39: Preliminary Analysis Results

## Slide 40: DC-DC Converter (MarcoA to provide Content)
Mass
Thermal
Reliability
Key parts volt/temp

## Slide 41: DC-DC Converter, Weight
Weight roll-up
Derating of critical parts (none?)

## Slide 42: DC-DC Converter, EMI-Filter
Filter performance simulations

## Slide 43: DC-DC Converter, Thermal Analysis
Thermal performance simulations (coolant, junction, temps)

## Slide 44: DC-DC Converter, Reliability Analysis
Reliability

## Slide 45: Energy Storage Device (ESD) (FrankP & RayS to provide content)
Mass
Thermal
Reliability – FP note: – Work with Yunasko
Key parts volt/temp – FP note: – Work with ESL

## Slide 46: Bio Break

## Slide 47: CAD Models

## Slide 48: EAU complete (RayS to provide content)

## Slide 49: EAU ICD

## Slide 50: EAU ICD (RayS to provide CONTENT)

## Slide 51: GUIs

## Slide 52: DC-DC Converter and ESD GUI (RayS to provide content)
Windows 10 based GUI
  Visual Studio 2013
  .Net Framework 4.7.2
Uses PCAN CAN/USB connection for comms
  CAN connects to Yunasko capacitors
  USB connects to computer with GUI
  500 kHz, Little Endian, MSB, Standard ID
Displays DC-DC Converter Info
Displays ESD Info
Sends Commands to DC-DC Converter
Path to aircraft [TBD]

## Slide 53: Long Lead Parts

## Slide 54: DC-DC Converter (MarcoA to provide content)
FP note: Parts & schedule
Heatsink (?), connectors (HBB, 20 wks), contactor (???)

## Slide 55: Capacitor Bank (FrankP to provide content)
FP note: Parts & schedule

## Slide 56: Capacitor Management System (CMS) (RayS to provide content)
FP note: This is a large section

## Slide 57: Risk Overview

## Slide 58: Program Risk (FrankP to add content)
Legend | 
Risk Score | 1 - 29
 | 30 - 69
 | 70 - 100
ID | Risk Description | Impact | Occ. | Sev. | Risk Score | Corrective Action | Owner | Status | Target Close Date
1 | Unresolved clarifications on specifications and requirements | Scope creep due to work scope not covered in SOW | 7 | 7 | 49 | 2.1 Review exceptions and assumptions during Kickoff 2.2 Schedule additional requirements review sessions post completion of internal EPT sessions | 2.1 Frank P 2.2 Frank S. | Open | 2.1 8/15 2.2 8/22
2 | Delay in receiving full battery specifications and requirements from Lockheed (will be released at time of LM RFP for F-35 Battery) | Potential for rework depending on extent of differences between current requirements and new release (e.g.. Software requirements) | 9 | 4 | 36 | 3.1 Build battery software to DO-178 DAL A standard 3.2 Use Integrated Project Team (LM/CRANE/EPT/AFRL) to review progress and provide feedback | 3.1 Frank P. 3.2 IPT | Open | 3.1 11/30 3.2 RFP Release

## Slide 59: Risk Management Matrix (FrankP to populate)
Occurrence | 10 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
 | 9 | 9 | 18 | 27 | 36 | 45 | 54 | 63 | 72 | 81 | 90
 | 8 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72 | 80
 | 7 | 7 | 14 | 21 | 28 | 35 | 42 | 49 | 56 | 63 | 70
 | 6 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54 | 60
 | 5 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
 | 4 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40
 | 3 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30
 | 2 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
 | 1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 |  | Severity |  |  |  |  |  |  |  |  | 
Risk Rate Schedule | 
Occurrence Ranking Criteria | Ranking
Nearly impossible, path does not exist for issue to occur | 1
Very low probability of occurrence | 2 - 3
Moderate probability of occurrence | 4 - 6
High probability of occurrence | 7 - 8
Very high probability of occurrence | 9 - 10
Severity Ranking Criteria | Ranking
No impact on project(cost or schedule)or product performance | 1
Less than 2% impact on project (cost and/or schedule); Minor deviations in product performance, but does not impede customer's expectations | 2 - 3
Between 2 - 9% impact on project (cost and/or schedule); Product performance deviations will cause non-conformance - relatively minor corrective actions required. | 4 - 6
Greater than 10% slip in schedule or cost; product non-conformance will result in need for major corrective action/ significant re-design required | 7 - 8
Greater than 15% slip in schedule or cost; produce does not meet customer's requirements - full re-deign required | 9 - 10

## Slide 60: Systems Engineering

## Slide 61: Compliance Matrix
Compliance Matrix excerpt below showing, how requirements and proposed changes are tracked and implemented. Note: embedded email top right, in customer change column.
EPT awaits Boeing’s feedback of the 87 TBR requirements submitted in November.

## Slide 62: Compliance Metrics
TBNs include TBD, TBR, TBS, TBP, & TBA
  TBD - To Be Determined
  TBR - To Be Reviewed / Resolved by Boeing
  TBS - To Be Suppled by Program PCKA, ESL, EPT
  TBP - To Be Provided by Customer Boeing
  TBA - To Be Announced
Note the high number of TBR (67%), due to requirements not being fully elicited during SRR. Total TBNs are at 83%
  Expectation is to burn down the number TBNs to 20% by CDR.
EPT will send the 22 conditionally compliant requirements to Boeing for review and disposition.

## Slide 63: Requirements Verification Traceability Matrix
The verification methods are being reviewed by Boeing, any changes will be reflected in the Acceptance Test Plan/Procedures.

## Slide 64: Requirements Verification Traceability Matrix
129 requirements
  8 Analysis
  22 Demonstration
  32 Inspection
  31 Test
  36 N/A
As the requirements are verified Verification status will be updated and if applicable the Objective Quality Evidence (OQE) will be embedded in to the Excel file.
  Either the actual OQE, e.g. test report or a hyperlink to the report will be embedded into the Excel file.
EPT will provide updated Excel upon request from Boeing for the purposes of monitoring the verification process progression.

## Slide 65: Identify KPPs
Note: All KPPs are in red and will be until the initial assessment
Once assessed KPPs will be tracked to ensure green status is reached and maintained
Preliminary table of KKPs are ready for submission to Boeing for review.

## Slide 66: Initial Test Plan
For this PDR phase there is one Acceptance test Plan/Procedure (ATP/P)
  Document number TBD.
The Acceptance Test Plan/Procedure is at a high level, i.e. Plan only.
  The ATP/P identifies the tests to be performed at the standard level, e.g. 5.1 Level 2 (DC-DC Converter) -40 to +160⁰F Temperature MIL-STD-810F Methods 501.4 (High temperature) Procedure II (Operating, Constant Temperature) and 502.4 (Low Temperature) Procedure II (Operating, constant temperature).
As the program progresses increased detail will be added to the point where there will be a complete detailed procedure.
It is expected that there will be separated procedures developed, for the many tests, along with the accompanying data sheets and test reports.
Testing will be performed IAW ATP/P and the detailed procedures that will follow. Any resulting failures will be analyzed to determine the root cause. Repairs will be made to return the EAU to the test program. It was agreed to by the customer on 2019 Dec 11 that a preliminary test plan is all that is required as exit criteria for PDR.

## Slide 67: Preliminary Test Facilities/Test configurations
To the right is Table 1 – Overall Program test Activity from the ATP/P
Test facilities are identified in BOLD.
Test configurations e.g. DC-DC Converter Component Level 4 are identified in test description.
Testing will follow the schedule contained in ATP/P resulting in two (2) EAUs for VIT testing per CDRL 3.4m. Customer agreed that EAU 1 will see every test identified in ATP/P while EAU 2 will see qualification op-vibe only.

## Slide 68: Test Equipment, instrumentation & Data Acquisition
FP note: Equipment / Location
The preliminary list of test assets listed will be adjusted as required for testing to yield the data required for analysis.

## Slide 69: Schedule

## Slide 70: Summarized Schedule (MichaelB to add schedule below)
FP note: Need a real, mpp schedule Alex B can help

## Slide 71: Key Deliverables (MichaelB to populate)
Objective:
  Complete design, development, and pre-qualification of a 270V battery to integrate with an agnostic interface to the F-35 Joint Strike Fighter
    CLIN 1: Conduct research and gather data
    CLIN 2: Deliver hardware
      Part A: 10 Battery Cell Modules; 18 Individual Battery Cells
      Part B: 14 Batteries; 12 Battery Cell Modules (with specified BMS Safety Features per SOW 6.1)
    CLIN 3: Non battery hardware and tooling
  Support NAVSEA/Crane testing (Test Readiness Reviews)

## Slide 72: Quarterly PMR’s and Design Review Schedule (MichaelB content)
Review Meeting | Location | Estimated Date
QMR Meeting 1 | Wright Patterson | 10/15/2019
QMR Meeting 2 | Joplin, MO | 1/15/2020
QMR Meeting 3 | East Greenwich, RI | 4/15/2020
QMR Meeting 4 | Wright Patterson | 7/15/2020
QMR Meeting 5 | Joplin, MO | 10/15/2020
QMR Meeting 6 | East Greenwich, RI | 1/15/2021
QMR Meeting 7 | Wright Patterson | 4/15/2021
QMR Meeting 8 | Joplin, MO | 7/15/2021
QMR Meeting 9 | East Greenwich, RI | 10/15/2021
Design Reviews Summary
Quarterly Management Reviews Summary
Subsystem | Review Meeting | Location | Estimated Date | Int/Ext
Battery | System Requirements Review | Joplin | 8/22/2019 | Ext
BMS | Preliminary Design Review | Joplin | May-20 | Ext
BMS | Critical Design Review | EG | Q2-2021 | Ext
Battery | Acceptance Testing Kickoff | EG | Sep-21* | Ext
Cell and Module | PDR | EG | Dec-19 | Ext
Cell and Module | CDR | EG | Q2-2020 | Ext
Battery | PDR |  | Q2-2020 | Ext
Battery | CDR | EG | Q2-2021 | Ext
Battery (Part A) | TRR |  | Q3-2020 | Ext
Battery (Part B) | TRR |  | Q4-2021 | Ext
*Prototype batteries are scheduled to be built (Q1 or Q2 2021)
Acceptance testing of the deliverable pre-qualification batteries is scheduled for Q4 2021. Which would AFRL be involved in as an Acceptance Test kickoff?

## Slide 73: Safety Tests

## Slide 74: RogerB to add content

## Slide 75: Specification Requirements Review

## Slide 76: RogerB to add content

## Slide 77: Program Management Plan

## Slide 78: Key Stakeholders (MichaelB to add content)
JSF Program Office
Wright Patterson/ Air Force Research Laboratory
  Customer lead facility and Program Point of Origin
Lockheed Martin (Fort Worth)
  ICD Definition (Effort led by NAVSEA Crane)
NAVSEA Crane
  Technical Lead
EaglePicher Locations
  East Greenwich:
    Cell Development
    Battery and Module Assembly
    Thermal Modeling
    Low Rate Manufacturing
  Joplin:
    Battery Management System (Hardware and Software)
    Manufacturing Ramp
Multi-site Effort

## Slide 79: EaglePicher Organizational Structure (Mburke to add content)
FP note: Insert updated org chart
Project Organization

## Slide 80: Communication Plan (MichaelB & RogerB to add content)
Documentation will be submitted according to CDRL schedule
File formats and requirements will be standard EP – except where called out in specifically
EP document control and QMS to be utilized for keeping track of documentation and adherence to standards (AS9100 and ISO)
CDRL | Title | Due Date
A001 | Scientific and Technical Reports | Draft: 30 days after TPOP end Final: 90 days after TPOP end
A002 | Funds and Man-Hour Expenditure Report | Monthly
A003 | Contractor Funds Status Report (CSFR) | Quarterly
A004 | Status Reports | Monthly
A005 | Presentation Materials | As Required
A006 | Assessment of Manufacturing Risk and Readiness | 30d after MRL Assessment
A007 | Conference Agenda | As Required
A008 | Conference Minutes | 3 days after PMRs
A009 | Interface Control Document | As Generated
A010 | Interface Requirements Specification | As Generated
A011 | Project Planning Chart | Monthly

## Slide 81: Weekly and Bi-Weekly Cadence (MichaelB to add content)
Weekly review of team progress and KPI tracking
Mechanical Process Lead
Chemical Process Lead
Systems Engineering Lead
Manufacturing Operations
Hardware Dev. Lead
Software Dev. Lead
EG TPM
JP TPM
Program Lead
Weekly Review (Wednesday afternoon – Thursday Morning)
Thursday Afternoon Internal Reviews
AFRL
JPO
NAVSEA CRANE
Lockheed Martin
External Stakeholders
Bi-weekly Friday Morning Reviews
ICD Int. Proj. Team
CRANE PM
ICD Cadence to be established as part of EPT/LM subcontract implementation

## Slide 82: Data Management Plan (FP note: who has this)
Quality Management System
  Internal EP process for managing documentation and manufacturing traceability
  Utilizes PDM software and ERP system for version control
  PDP Phase reviews will be audited by EPT’s centralized Quality Assurance team
File formats
  Standard formats will be utilized to communicate reports
    MS Office
    .pdf
    Password protected as necessary
Configuration Control
  Will adhere to LM standards
  DOORS software used to manage flow-down of customer requirements (linkage to sub-tier requirements)

## Slide 83: Program Metrics
In line with CDRL A002 – Contract Funds and Expenditure Report
Key Metrics
  Direct and Indirect Cost to Date
    Total Hours (Salaried and Hourly)
    Materials and Services Expenditures
  Progress Trend (Percent Complete relative to schedule and program deliverables)
  Estimate To Completion
    Based on variance – should also include analysis of deviations and risk analysis/mitigation
Earned Value Management

## Slide 84: Action Items

## Slide 85: Action Items Review

## Slide 86: Backup Slides